## Slide 1: Disaster data: OSM POI data with stable IDs for emergency planning
14/11/2025
how the NCCN uses OSM & authentic sources in Paragon

## Slide 2: What is Paragon?
What is a security platform?
  Cooperation between police, fire fighters, medical staff, logistics and communication
  Crisis/national preparation + Crisis management
  + Database of emergency plans
Tackle a crisis as soon as possible!
National security platform
Notes: Map based interface
Activate during specific crisis to keep track of situation on the ground and communicate core information

## Slide 3: DATA FOR Paragon
Multiple basemaps (default OSM tiles)
Overlays with Anchors (POIs) which can be interacted with & can be linked
Emergency Plans containing locations & contacts that might become relevant
Cases get ad hoc Anchors or re-use existing ones
Map-centric interface
Notes: Map centered tool - getting a common operational picture
OSM as a basemap is kind of obvious for us here, but less obvious in the federal government environment

## Slide 4: External POI data in paragon
Using official data?
Or using publicly crowdsourced data?
Using the data our own users generate?
Notes: The precursor application only used data provided by the users
Big problems with regional differences in quality, lack of maintenance and standardization
Official data to the rescue?
Or do public crowdsourcing?

## Slide 5: WHICH SOURCES TO USE?
Why use official data?
Strength
  Complete*
  Standardized (within the region)
  Standardized update cycle
Weakness
  Administrative reality
  Different between regions
  Slow update cycle
  Geocoded address
Notes: *: for what is in the administrative scope
“this case is not in the data because it doesn’t fit our world view” (e.g. temporary school, school is not subsidized)
Logic based on administrative processes; e.g. a school is not a site

## Slide 6: WHICH SOURCES TO USE?
Why use OpenStreetMap data?
Strength
  Detailed polygons
  As you see it in reality
  Continuous updates
  Precise geometry
  Global data model (with local “dialects”)
Weakness
  Limited on attributes (e.g. contact details)
  Unstructured maintenance process
  Completeness and detail very variable between places
Notes: Need to go cross-border with our application
Note: not just OSM, also Wikidata to some degree

## Slide 7: WHICH SOURCES TO USE?
Por que no los dos?
Notes: Summarize the official data
Link to OSM data if available
Based on location, name, address, some attributes
Combine to build something better than the parts

## Slide 8: Filtering: sports example
Start with all sports related facilities (N: 240.047)
Remove private pools (N: 202.324)
Remove tracks & pitches without a name (N: 63.488)
Remove amenities used in other processes (N: 63.354)
Merge all overlapping features’ info on outer polygon (N: 56.295)
Remove if still no name (N: 34.225)

## Slide 9: Anchor source types
OFFICIAL DATA ONLY
Seveso sites
Pipelines
Nuclear installations
Seaports
Bus & tram stops
Town halls
Nurseries
Asylum reception
Water sensors
Nuclear radiation sensors
Rivers
Summer camps
High voltage pylons
OSM ONLY
Hospitals*
Firestations*
Airports*
Prisons*
Cultural centres*
Sports
Religious buildings
Train stations
Metro stations
Wind turbines*
Asylum detention*
Locks & dams
Civil protection
Shopping malls
Power stations
High voltage lines
MIXED DATA
Schools
Police stations
Care for the disabled
Nursing homes
Notes: So in the end, a lot of data comes either from official data sources (italic is public data)
many layers are pure OSM data
Relatively few mixed data, because of added complexity – but with new modular approach it became easier
Hospitals: will be merged in the future
*: OSM data validated with official sources

## Slide 10: The data management problem
Notes: How to handle 35 different ingestion processes with monthly updates & high QA necessity & lots of user feedback?
Simple common resulting data structure for all the datasets
Processes that try to re-use techniques and preferably code blocks
Modular processes, e.g. generic compare dataset process, generic “merge official point to OSM polygon” module
Run processes automatically using Airflow
Bulk analyze results & monthly release cycle of all the sources at once

## Slide 11: External POI data in paragon
Need for stable IDs!
Anchors are for linking
Add location to your Cases & Emergency Plans
Notes: Unique IDs are not a uniquely OSM problem
The same ID in the source does not always mean we would like to consider it the same object. E.g. a police station that moved may no longer be relevant for an emergency plan for a specific zone

## Slide 12: The UNIQUE ID problem
Notes: Start by processing new data. Maybe just filtering, simplification & restructuring. Maybe includes conflating different sources
At the end we have an “ingestion table” where everything has a new UUID
If the layer is now, we copy straight to the Anchor database
For updating, we use a generic process:
  Check if the same original ID still represents the same object > lightens computing load
  The rest become candidates for fuzzy match. Found a single good candidate? > updated
  No candidate? New/deleted objects

## Slide 13: THE DATA QUALITY PROBLEM
Working on better data
With official sources
With the OSM community
Notes: For official sources… well it’s hard
Some minor success
Often not even a reply to an email
For OSM data: appears a lot easier. But unique challenges too

## Slide 14
Notes: Some manual reviewing of OSM data
Adding extra tags to clarify things, like
- type of fire station
- international airport vs any old airstrip
- hospital heliports

## Slide 15: OSM projects
Review all firestations
Check police stations not in official data
Cultural center fixup
Hospitals
  Check completeness & add official IDs
  Standardize heliports
  Add emergency ward entrances
Schools: sites without a name, add missing schools
Places of worship: filtering out the small stuff
Notes: * Includes minor data model extensions

## Slide 16: MapRoulette
Turn all issues into microtasks
With management dashboard
6 big challenge, over 1500 tasks finished = 254 hours of work = two months FTE

## Slide 17: Common mistakes – mapping for the render
Notes: Tags “for rendering” on the outline, but then also some or all tags on the building
Amenity only needed once!

## Slide 18: Common mistakes - overenthousiasm
Notes: Overly enthusiastic mapping: adding things as what they will be, not as what they are

## Slide 19: Common annoyances – everything is a (unqualified) thing
Chart: 
| large | small | likely large | likely small | no idea
place_of_worship | 43 | 405 | 0 | 0 | 0
place_of_worship:type | 0 | 84 | 0 | 0 | 0
building | 20277 | 7913 | 0 | 0 | 0
building_part | 50 | 37 | 0 | 0 | 0
historic | 4 | 966 | 2 | 12 | 1
service_times | 3098 | 0 | 0 | 0 | 0
name | 0 | 0 | 3088 | 1886 | 0
lack of name and relgion | 0 | 0 | 0 | 293 | 0
muslim | 0 | 0 | 570 | 0 | 0
none | 0 | 0 | 0 | 0 | 6361
Notes: Everything is a place of worship
It’s hard to identify which are big
14% we have no idea
Another 13% we can only make an educated guess

## Slide 20: Wanna help?
https://maproulette.org/browse/projects/54664
Supports OpenStreetMap Belgium as a Corporate Member

## Slide 21: Paragon data team: paragon-data@nccn.fgov.be Help us improve OSM https://maproulette.org/browse/projects/54664 Use our code https://github.com/joostschouppe/NCCN-anchor-processing https://en.osm.town/@joost_schouppe
https://crisiscentrum.be @CrisiscenterBE
Notes: Help us improve OSM for national crisis management